## Slide 1: Data Representation & Boolean Algebra

## Slide 2
Number system
Different Number system
Base / Radix
MSD / LSD
Number Conversion
Binary Arithmetic
Representation of Numbers
Representation of Characters
Boolean Algebra
Demorgan’s Theorm

## Slide 3: Number system
Systematic way to represent numbers in different ways
Hello world
01001000 01100101 01101100 01101100 01101111 00100000 01110111 01101111 01110010 01101100 01100100
72 101 108 108 111 32 87 111 114 108 100

## Slide 4: Different types of Number system
Binary Number system
  0, 1
Octal Number system
  0, 1, 2, 3, 4, 5, 6, 7
Decimal Number system
  0, 1, 2, 3, 4, 5, 6, 7, 8, 9
Hexadecimal Number system
    0, 1, 2, 3, 4, 5, 6, 7, 8, 9,
    A, B, C, D, E, F

## Slide 5: Base / Radix
The number of symbols used in a number system is called Base / Radix of a number system
Eg. (1301)
8

## Slide 6
Identify the number system
(1102)
(1101)
(6327)
16
10
8
Hexadecimal
Octal
Decimal

## Slide 7: MSD & LSD
MSD : Left most digit of a number is called MSD
( Most Significant Digit )
LSD : Right most digit of a number is called LSD
( Least Significant Digit )

## Slide 8: - Binary Number system
Base : 2
Symbols : 0 1
Also called BIT
Eg : (1101)
Position Representation
2

## Slide 9: - Binary Number system
Eg : (1101.11)
Position Representation
2

## Slide 10: - Octal Number system
Base : 8
Symbols : 0 1 2 3 4 5 6 7
Eg : (1372)
Position Representation
8

## Slide 11: - Octal Number system
Eg : (1372 . 25)
Position Representation
8

## Slide 12: - Decimal Number system
Base : 10
Symbols : 0 1 2 3 4 5 6 7 8 9
Eg : (1902)
Position Representation
10

## Slide 13: - Decimal Number system
Eg : (1902 . 18)
Position Representation
10

## Slide 14: - Hexadecimal Number system
Base : 16
Symbols : 0 1 2 3 4 5 6 7 8 9 A B C D E F
Eg : (1B04)
Position Representation
16

## Slide 15: - Hexadecimal Number system
Eg : (1B04 . F6)
Position Representation
16

## Slide 16: Number Conversion
Convert one number system to another number system

## Slide 17
Binary to Decimal
Octal to Decimal
Hexadecimal to Decimal
Decimal to Binary
Decimal to Octal
Decimal to Hexadecimal
Octal to Binary
Hexadecimal to Binary
Binary to Octal
Binary to Hexadecimal
Octal to Hexadecimal
Hexadecimal to Octal

## Slide 19
Binary to Decimal
Octal to Decimal
Hexadecimal to Decimal
( )
( )
( )
2
8
16
( )
10
    - Multiplication Method

## Slide 20
Decimal to Binary
Decimal to Octal
Decimal to Hexadecimal
( )
( )
( )
2
8
16
( )
10
    - Repeated Division Method

## Slide 21
Octal to Binary
Hexadecimal to Binary
( )
( )
8
16
( )
2
    - Conversion Method

## Slide 22
Binary to Octal
Binary to Hexadecimal
( )
( )
8
16
( )
2
    - Grouping Method

## Slide 23
Octal to Hexadecimal
Hexadecimal to Octal
( )
( )
8
16
( )
2
    Covert to Binary
    then Binary to Number system
( )
( )
8
16
( )
2

## Slide 24: Number Conversion Lets Starts…

## Slide 25: - Binary to Decimal Conversion
Multiply each bits by its positional value and add
Eg : convert (1101.11) to Decimal.
Position Representation
2

## Slide 26: - Binary to Decimal Conversion
a
b
(1101.11) = (13.75)
2
10

## Slide 28: - Octal to Decimal Conversion
Multiply each octal digit by its positional value and add
Eg : convert (256.11) to Decimal.
Position Representation
8
2
8
2
5
8
1
6
8
0
.
Octal Point
1
8
-1
1
8
-2

## Slide 29: - Octal to Decimal Conversion
(256.11) = (113.1406)
8
a
b
2
8
2
5
8
1
6
8
0
.
1
8
-1
1
8
-2
+
2 x 8
2
5 x 8
1
=
a
+
6 x 8
0
+
64
40
=
+
9
=
113
+
1 x 8
-1
1 x 8
-2
=
b
= 0.125 + 0.0156
= 0.1406
10

## Slide 31: - Hexadecimal to Decimal Conversion
Multiply each hexadecimal digit by its positional value and add
Eg : convert (3A6.13) to Decimal.
Position Representation
16
3
16
2
A
16
1
6
16
0
.
Hexadecimal Point
1
16
-1
3
16
-2

## Slide 32: - Hexadecimal to Decimal Conversion
(256.11) = (934.0665)
16
a
b
a = 3 x 16 + (10) x 16 + 6 x 16
2
=
934
+
1 x 16
-1
3 x 16
-2
=
b
= 0.0625 + 0.004
= 0.0665
10
3
16
2
A
16
1
6
16
0
.
1
16
-1
3
16
-2
1
0
= 768 + 160 + 6

## Slide 34: - Decimal to Binary Conversion
Repeatedly dividing it by 2, until the quotient is zero
Reminder generate each division form binary number
Eg : convert (25 . 28) to Binary.
Position Representation
10
2
10
1
5
10
0
.
Decimal Point
2
10
-1
8
10
-2

## Slide 35: - Decimal to Binary Conversion
A
B
2
10
1
5
10
0
.
2
10
-1
8
10
-2
2 25
2 12 1
2 6 0
2 3 0
2 1 1
0 1
MSB
LSB
A
A = 11001

## Slide 36: - Decimal to Binary Conversion
A
B
2
10
1
5
10
0
.
2
10
-1
8
10
-2
B = 01000
Fractional part conversion by multiply with 2
0.28 x 2 = 0.56 0
0.56 x 2 = 1.12 1
0.12 x 2 = 0.24 0
0.24 x 2 = 0.48 0
0.48 x 2 = 0.96 0
LSB
MSB
B
(25.28) = (11001.01000)
10
2

## Slide 38: - Decimal to Octal Conversion
Repeatedly dividing it by 8, until the quotient is zero
Reminder generate each division form Octal number
Eg : convert (163 . 253) to Octal.
Position Representation
10
6
10
1
3
10
0
.
Decimal Point
2
10
-1
5
10
-2
1
10
2
3
10
-3

## Slide 39: - Decimal to Octal Conversion
A
B
8 163
8 20 3
8 2 4
8 0 2
MSB
LSB
A
A = 243
6
10
1
3
10
0
.
2
10
-1
5
10
-2
1
10
2
3
10
-3

## Slide 40: - Decimal to Octal Conversion
B = 20142
Fractional part conversion by multiply with 8
0.253 x 8 = 2.024 2
LSB
MSB
B
(163.253) = (243 . 20142 )
10
8
A
B
6
10
1
3
10
0
.
2
10
-1
5
10
-2
1
10
2
3
10
-3
0.024 x 8 = 0.192 0
0.192 x 8 = 1.536 1
0.536 x 8 = 4.288 4
0.288 x 8 = 2.304 2

## Slide 42: - Decimal to Hexadecimal Conversion
Repeatedly dividing it by 16, until the quotient is zero
Reminder generate each division form Hexadecimal number
Eg : convert (298 . 653) to Octal.
Position Representation
10
9
10
1
8
10
0
.
Decimal Point
6
10
-1
5
10
-2
2
10
2
3
10
-3

## Slide 43: - Decimal to Hexadecimal Conversion
16 18 10
A
B
MSB
LSB
A
A = 12 (10)
9
10
1
8
10
0
.
6
10
-1
5
10
-2
2
10
2
3
10
-3
16 298
16 1 2
0 1
= 12 A

## Slide 44: - Decimal to Hexadecimal Conversion
B = (10) 7 2 (11)
Fractional part conversion by multiply with 16
0.653 x 16 = 10.448 10
LSB
MSB
B
(298 . 653) = (12A . A72B)
10
16
0.448 x 16 = 7.168 7
0.168 x 16 = 2.668 2
0.668 x 16 = 11.008 11
A
B
9
10
1
8
10
0
.
6
10
-1
5
10
-2
2
10
2
3
10
-3
= A72B

## Slide 46: - Octal to Binary Conversion
Covert each Octal digit into its 3 bit binary equivalent
Octal | Binary Equivalent
0 | 000
1 | 001
2 | 010
3 | 011
4 | 100
5 | 101
6 | 110
7 | 111

## Slide 47: - Octal to Binary Conversion
A
B
A
11 101 . 001
3
8
1
5
8
0
.
1
8
-1
0
8
-2
Eg : Convert (35 . 10) to Binary
8
B
(35.10) = (11101. 001)
10
2
011 101 . 001 000
3 5 . 1 0

## Slide 49: - Hexadecimal to Binary Conversion
Covert each Hexadecimal digit into its 4 bit binary equivalent
Hexadecimal | Binary Equivalent
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
A | 1010
B | 1011
C | 1100
D | 1101
E | 1110
F | 1111

## Slide 50: - Hexadecimal to Binary Conversion
A
B
A
110 1010 . 0010 0001
6
16
1
A
16
0
.
2
16
-1
1
16
-2
Eg : Convert (6A . 21) to Binary
16
B
(6A.21) = (1101010 . 00100001)
16
2
0110 1010 . 0010 0001
6 A . 2 1

## Slide 52: - Binary to Octal Conversion
Covert 3 bit Binary number into corresponding Octal equivalent
Binary | Octal Equivalent
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7

## Slide 53: - Binary to Octal Conversion
Eg : Convert (1100110 . 01) to Octal
2
(1100110 . 01) = (146. 2)
2
8
1 100 110 . 01
001 100 110 . 010
1 4 6 . 2

## Slide 55: - Binary to Hexadecimal Conversion
Covert 3 bit Binary number into corresponding Octal equivalent
Binary | Hexadecimal Equivalent
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
1000 | 8
1001 | 9
1010 | A
1011 | B
1100 | C
1101 | D
1110 | E
1111 | F

## Slide 56: - Binary to Hexadecimal Conversion
Eg : Convert (1100110 . 01) to Hexadecimal
2
(1100110 . 01) = (66 . 4)
2
16
110 0110 . 01
6 6 . 4
0110 0110 . 0100

## Slide 58: - Octal to Hexadecimal Conversion
Convert octal number into equivalent binary,
then convert binary to hexadecimal
Eg : Convert (67. 4) to Hexadecimal
8
6 7 . 4
110 111 . 100
3 7 . 8
11 0111 . 100
0011 0111 . 1000
Octal to Binary
Binary to Hexadecimal
(67.4) = (37.8)
8
16

## Slide 60: - Hexadecimal to Octal Conversion
Convert Hexadecimal number into equivalent binary,
then convert binary to Octal
Eg : Convert (B6. F) to Octal
16
B 6 . F
1011 0110 . 1111
2 6 6 . 7 4
10 110 110 . 111 1
Hexadecimal to Binary
Binary to Octal
(B6.F) = (266.74)
16
8
010 110 110 . 111 100

## Slide 62: Binary Arithmetic

## Slide 63
Binary Addition
Binary Subtraction

## Slide 64: - Binary Addition
Carry bit 1 is created only two 1s are added
Three 1s are added ,then sum is 1 and carry is 1
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
0 +
0
0
0 +
1
1
1 +
0
1
1 +
1
10
1 +
1
1
11

## Slide 65
Eg : Find sum of binary numbers 1011 and 1001
1 0 1 1 +
1 0 0 1
1 0 1 0 0
1 1

## Slide 66
Eg : Find sum of binary numbers 110111 and 111
1 1 0 1 1 1 +
1 1 1
1 1 1 1 1 0
1 1 1

## Slide 68: - Binary Subtraction
Borrow bit 1 is created only 1 subtracted from 0
A | B | Difference | Borrow
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0

## Slide 69
Eg : Subtract 10101 from 11111
1 1 1 1 1 -
1 0 1 0 1
0 1 0 1 0

## Slide 70
Eg : Subtract 011 from 101
1 0 1 -
0 1 1
0 1 0
5 -
3
2
0 2

## Slide 71
Eg : Subtract 10111 from 101000
1 0 1 0 0 0 -
1 0 1 1 1
0 1 0 0 0 1
0 2
1 2
1 2
0 2

## Slide 73: Representation of Numbers

## Slide 74
Numbers or integers represented in computer are
  Sign and Magnitude Representation ( SM )
  1’s Compliment Representation
  2’s Compliment Representation

## Slide 75: - Sign and Magnitude Representation
It is used to represent signed numbers
It consist of sign part and magnitude part
Example : - 32 +51 - 7
A Computer word size is 1 byte (8 bit)
The 7th bit (MSD) is used for representing sign of a number
Sign Part
Magnitude Part
Magnitude
Sign
MSD
LSD
0
0
0
0
0
0
0
0

## Slide 76
If 7th bit is Zero , it indicate the number is +ve
If 7th bit is One , it indicate the number is -ve
0
0
0
0
0
1
0
1
+
5
+5
1
0
0
0
0
1
0
1
-
5
-5

## Slide 78: - 1’s Compliment Representation
Another method of representing Negative numbers
-ve number indicate its compliment
0
0
0
0
0
1
0
1
+5
1
1
1
1
1
0
1
0
-5
1’s Compliment

## Slide 80: - 2’s Compliment Representation
Another method of representing Negative numbers
Just add 1 with 1’s compliment
0
0
0
0
0
1
0
1
+5
1
-5
1
1
1
1
1
0
1
0
1’s Compliment
1
1
1
1
1
0
1
1
2’s Compliment

## Slide 82: Representation of Characters

## Slide 83
Symbolic way to represent characters in computers are called character representation
  ASCII
  EBCDIC
  ISCII
  Unicode

## Slide 84: ASCII
ASCII
American Standard Code for Information interchange
Use 7 bit to represent a character
Example : A 97 ( 1 1 0 0 0 0 1 )
It can represent 128 characters
2 = 128
7

## Slide 85: EBCDIC
  EBCDIC
  Extended Binary Coded Decimal Interchange Code
  Similar to ASCII
Use 8 bit to represent a character
It can represent 256 characters
2 = 256
8

## Slide 86: ISCII
  ISCII
  Indian Standard Code for Information Interchange
  Or Indian Script Code for Information Interchange
Use 8 bit to represent a character
It can be used to represent various writing system of india

## Slide 87: Unicode
  Unicode
  16 bit Code represent up to 65,536 characters
  Used to represent almost all written languages of the world
  Now a days Unicode represent more than 16 bit codes

## Slide 89: Boolean Algebra

## Slide 90: Boolean Algebra
Boolean algebra is a form of mathematics that deals with statements and their values.
It can have only two values: true or false. ( 0 or 1 )
The operation performed by Boolean values are called Boolean operations / logical operations
Logical gate : physical device that perform logical operations
It is implemented using diodes and transistors

## Slide 91: Boolean Operations and logical gates
3 basic Boolean operations in Boolean algebra
  OR  Logical Addition
  AND  Logical Multiplication
  NOT  Logical Negation

## Slide 92: Logical OR
OR operation performs logical addition
+ Plus symbol used for this operation
A + B read as A OR B
Truth table : ( All possible operations and results )
Input A | Input B | Y = A + B (A OR B)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 93
OR Gate
OR Gate Circuit
“ If any one of the input is true, the total output is true ”

## Slide 94: Logical AND
AND operation performs logical Multiplication
. Dot symbol used for this operation
A . B read as A AND B
Truth table : ( All possible operations and results )
Input A | Input B | Y = A . B (A AND B)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 95
OR Gate
OR Gate Circuit
“ If both of the input is true, the total output is true ”

## Slide 96: Logical NOT
NOT operation performs logical Nagation
over bar symbol used for this operation
A read as A NOT
Truth table : ( All possible operations and results )
Input A | Y = A
0 | 1
1 | 0
Also called inverter

## Slide 97
OR Gate
OR Gate Circuit
“ output give the complement of input”
A
Y = A

## Slide 99: Principle of Duality
A Boolean relation can be written to another Boolean relation by changing each OR operation to AND operation vice versa
Example : A ( B + C ) = AB . AC
If the statement is true for an expression, then it is also true for the dual of the expression

## Slide 101: Basic theorems of Boolean Algebra
Standard and accepted rules in Boolean algebra
The rules are known as axioms
  Identity law
  Idempotent law
  Involution law
  Complimentary law
  Commutative law
  Associative law
  Distributive law
  Absorption law

## Slide 102: Identity law
Additive identity
Multiplicative identity
  0 + x = x 1 + x = 1
  0 . x = 0 1 . x = x
  0 + x = x 1 + x = 1
  0 + 0 = 0 1 + 0 = 1
  0 + 1 = 1 1 + 1 = 1
  0 . x = 0 1 . x = x
  0 . 0 = 0 1 . 0 = 0
  0 . 1 = 0 1 . 1 = 1

## Slide 103: Idempotent law
  x + x = x
  x . x = x
  x + x = x
  0 + 0 = 0
if x = 0 ,
  x + x = x
  1 + 1 = 1
if x = 1 ,
  x . x = x
  0 . 0 = 0
if x = 0 ,
  x . x = x
  1 . 1 = 1
if x = 1 ,

## Slide 104: Involution law
  X = X
if x = 0 ,
  X = X
  0 = 1
  0 = 0
if x = 1 ,
  X = X
  1 = 0
  1 = 1

## Slide 105: Complimentary law
  X + X = 1
  X . X = 0
if x = 0 ,
  x + x = 1
  0 + 0
  1 + 0 = 1
if x = 1 ,
  x + x = 1
  1 + 1
  0 + 1 = 1
if x = 0 ,
  x . x = 0
  0 . 0
  1 . 0 = 0
if x = 1 ,
  x . x = 0
  1 . 1
  0 . 1 = 0

## Slide 106: Commutative law
  x + y = y + x
  x . y = y . x
X | Y | X + Y | Y + X
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1
X | Y | X . Y | Y . X
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 1 | 1

## Slide 107: Associative law
  x + ( y + z ) = ( x + y ) + z
  x . ( y . z ) = ( x . y ) . z

## Slide 108
  x + ( y + z ) = ( x + y ) + z
X | Y | Z | Y + Z | X + (Y + Z) | X + Y | (X + Y) + Z
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 109
  x . ( y . z ) = ( x . y ) . z
X | Y | Z | Y . Z | X . (Y . Z) | X . Y | (X . Y) . Z
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 110: Distributive law
  x . ( y + z ) = ( x . y ) + ( x . z )
  x + ( y . z ) = ( x + y ) . ( x + z )

## Slide 111
  x . ( y + z ) = ( x . y ) + ( x . z )
X | Y | Z | Y + Z | X . (Y + Z) | X . Y | X . Z | (X . Y) + ( X . Z )
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 112
  x + ( y . z ) = ( x + y ) . ( x + z )
X | Y | Z | Y . Z | X + (Y . Z) | X + Y | X + Z | (X + Y) . ( X + Z )
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 113: Absorption law
  x + ( x . y ) = x
  x . ( x + y ) = x
X | Y | X . Y | X + (Y . X)
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1
X | Y | X + Y | X . (Y + X)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1

## Slide 115: De Morgan’s theorems

## Slide 116: De Morgan's theorems
The Complement of sum of Boolean variable is equal to product of their individual complements.
X + Y = X . Y
The Complement of product of Boolean variable is equal to sum of their individual complements.
X . Y = X + Y

## Slide 117
Proof of 1st theorem
X + Y = X . Y
7
8

## Slide 118
Equation 7 :

## Slide 119
Equation 8 :

## Slide 120
Proof of 2nd theorem
7
8
X . Y = X + Y

## Slide 121
Equation 7 :

## Slide 122
Equation 8 :

## Slide 124: Logic Circuits

## Slide 126: Universal gate
Universal gate is a gate which can implement any other Boolean function without using any other gates
NAND gate and NOR gate are called universal gate.
NAND = Noted AND gate

## Slide 127: Universal gate
NOR = Noted OR gate
A
B
A+B
A+B
A+B
A
B

## Slide 130
Teaching materials Prepared by
RIDHUN DEV
Lecture IHRD College
+1 / +2 Computer Science
8089552581